Turris Omnia - description of I2C communication between MCU (STM32) and CPU (Marvell)

### Address, timing
- current I2C address of MCU
  - 0x2A
- I2C timing / speed
  - 100kHz

### Commands

enum i2c_commands {
    CMD_GET_STATUS_WORD = 0x01, /* slave sends status word back */
    CMD_GENERAL_CONTROL = 0x02,
    CMD_LED_MODE = 0x03, /* default/user */
    CMD_LED_STATE = 0x04, /* LED on/off */
    CMD_LED_COLOUR = 0x05, /* LED number + RED + GREEN + BLUE */
    CMD_USER_VOLTAGE = 0x06,
    CMD_SET_BRIGHTNESS = 0x07,
    CMD_GET_BRIGHTNESS = 0x08
};

### Communication

### Data types
status_word
/*
 * Bit meanings in status_word:
 * Bit Nr. | Meanings
 * -----------------
 * 0 | SFP_DET : 1 - SFP detected, 0 - SFP not detected
 * 1 | SFP_LOS : 1 - SFP receiver lost signal, 0 - no lost
 * 2 | SFP_FLT : 1 - SFP trasmitter fault, 0 - no TX fault
 * 3 | SFP_DIS : 1 - SFP TX disabled; 0 - SFP TX enabled
 * 4 | CARD_DET : 1 - mSATA/PCIe card detected, 0 - no card
 * 5 | mSATA_IND : 1 - mSATA card inserted, 0 - PCIe card inserted
 * 6 | USB30_OVC : 1 - USB3-port0 overcurrent, 0 - no overcurrent
 * 7 | USB31_OVC : 1 - USB3-port1 overcurrent, 0 - no overcurrent
 * 8 | USB30_PWRON : 1 - USB3-port0 power ON, 0 - USB-port0 power off
 * 9 | USB31_PWRON : 1 - USB3-port1 power ON, 0 - USB-port1 power off
 * 10 | ENABLE_4V5 : 1 - 4.5V power is enabled, 0 - 4.5V power is disabled
 * 11 | BUTTON_MODE : 1 - user mode, 0 - default mode (brightness settings)
 * 12 | BUTTON_PRESSED : 1 - button pressed in user mode, 0 - button not pressed
 * 13..15 | BUTTON_COUNT : number of pressing of the button (max. 7) - valid in user mode
*/

Example of reading status word from Linux:

„i2cget 1 0x2A 1 w“

Meanings:
1 – i2cbus number
0x2A – I2C address of the slave
1 – „address of register“ = command
w – word data type

control_byte

/*
 * Bit meanings in control_byte:
 * Bit Nr. | Meanings
 * -----------------
 * 0 | LIGHT_RST : 1 - do light reset, 0 - no reset
 * 1 | HARD_RST : 1 - do hard reset, 0 - no reset
 * 2 | FACTORY_RST : 1 - do factory reset, 0 - no reset
 * 3 | SFP_DIS : 1 - SFP TX disabled; 0 - SFP TX enabled
 * 4 | USB30_PWRON : 1 - USB3-port0 power ON, 0 - USB-port0 power off
 * 5 | USB31_PWRON : 1 - USB3-port1 power ON, 0 - USB-port1 power off
 * 6 | ENABLE_4V5 : 1 - 4.5V power supply ON, 0 - 4.5V power supply OFF
 * 7 | BUTTON_MODE : 1 - user mode, 0 - default mode (brightness settings)
*/

Example of setting of control byte (perform light reset):

“i2cset 1 0x2A 2 1 b”

Meanings:
1 – i2cbus number
0x2A – I2C address of the slave
2 – „address of register“ = command
1 – do light reset
b – byte data type

led_mode_byte – default or user led mode
! Note: Order of the LEDs is reversed! LED0 is USER_LED2 and LED11 is POWER_LED
/*
 * Bit meanings in led_mode_byte:
 * Bit Nr. | Meanings
 * -----------------
 * 0..3 | LED number [0..11] (or in case setting of all LED at once -> LED number = 12)
 * 4 | LED mode : 1 - USER mode, 0 - default mode
 * 5..7 | dont care
*/
Example of setting of LED mode (user mode on LED10 = LAN1):

“i2cset 1 0x2A 3 0x1A b”

Meanings:
1 – i2cbus number
0x2A – I2C address of the slave
3 – „address of register“ = command
0x1A – LED1 set to user mode
b – byte data type

led_state_byte – LED can be set to OFF/ON state

/*
 * Bit meanings in led_state_byte:
 * Bit Nr. | Meanings
 * -----------------
 * 0..3 | LED number [0..11] (or in case setting of all LED at once -> LED number = 12)
 * 4 | LED mode : 1 - LED ON, 0 - LED OFF
 * 5..7 | dont care
*/

Example of setting of LED state (LED10 set to ON):
Note: LED10 was set to user mode in previous step.

“i2cset 1 0x2A 4 0x1A b”

Meanings:
1 – i2cbus number
0x2A – I2C address of the slave
4 – „address of register“ = command
0x1A – LED1 set to ON
b – byte data type

led_colour – set colour for LEDs

/*
 * Bit meanings in led_colour:
 * Byte Nr. | Bit Nr. | Meanings
 * -----------------
 * 1.B | 0..3 | LED number [0..11] (or in case setting of all LED at once->LED number=12)
 * 1.B | 4..7 | dont care
 * 2.B | 8..15 | red colour [0..255]
 * 3.B | 16..23 | green colour [0..255]
 * 4.B | 24..31 | blue colour [0..255]
*/

Example of setting of LED10 colour – green colour = 0x00FF00:

“i2cset 1 0x2a 5 0x0A 0x00 0xFF 0x00 i”
Meanings:
1 – i2cbus number
0x2A – I2C address of the slave
5 – „address of register“ = command
0x0A - LED10
0x00 0xFF 0 x00 – red colour = 0x00, green = 0xFF, blue = 0x00
i – word data type

- brightness_byte – brightness settings for LEDs
  - value in range 0..100 [%]

a) Example of setting to 20% brightness:

“i2cset 1 0x2A 7 20 b”

Meanings:
1 – i2cbus number
0x2A – I2C address of the slave
7 – „address of register“ = command
20 – brightness [%]
b – byte data type

b) Reading of brightness:
“i2cget 1 0x2A 8 b”

Meanings:
1 – i2cbus number
0x2A – I2C address of the slave
8 – „address of register“ = command
b – byte data type

user_voltage_byte – voltage setup on user regulator
enum voltage_values {
    VOLTAGE_33 = 1,
   VOLTAGE_36 = 2,
    VOLTAGE_45 = 3,
    VOLTAGE_51 = 4,
};

Example of setting 3.3V on user regulator:

1.step: enable regulator (using control_byte)
“i2cset 1 0x2A 2 0x40 b”

Meanings:
1 – i2cbus number
0x2A – I2C address of the slave
2 – „address of register“ = command
0x40 – enable regulator
b – byte data type

2.step: set desired voltage
“i2cset 1 0x2A 6 1 b”

Meanings:
1 – i2cbus number
0x2A – I2C address of the slave
8 – „address of register“ = command
1 – enum value for 3.3V
b – byte data type